## Slide 1: Foras Promineo Software

## Slide 2: What is a cubesat / foras promineo 

## Slide 3: Block of how it operates in space

## Slide 4: Conops
Host PC software
Ground Station PC Software
Satellite Software
Website

## Slide 5: Satellite Software Preface
Satellite programming is mostly in circuitpython. Firmware is written in C, but Caden has taken care of that. (mostly just pin definitions anyways…)
Satellite programming is for a MICROCONTROLLER, so it is MUCH less powerful and fast than a PC!!
  i.e. during normal execution there is <1MByte of RAM available for task execution.
  Floating point is MUCH slower than integer operations
  Data transactions over the radio are limited to 256 byte packets.
  UART interface to payload is running at ~1MHz but is unverified.
Good practice is to just be mindful of what resources / typing your code is using.
  Since python is dynamically typed, type casting in this application is quite important!
    i.e. differences between a bool, int, float, and string object.
    Also be aware of various decorations like the 0x (hex) or b’’ (binary) prefix, or @property.setters

## Slide 6: Preface (cont.)
A lot of the backround lower-level libs have been written by Max Alvarez (guy who developed pycubed architecture) or wrote and modified by Caden (me)

## Slide 7: Using Github for software slide

## Slide 8: Project File Structure
Top Level:
cdh, boot, and main files
Task Directory:
Tasks
Lib Directory:
All lib files for usage. Each lib follows a fairly similar format

## Slide 9
Master Library
Init routine initializes each device in self.hardware
Each initialization for the devices is within its own try – except clause.
Hardware dictionary for each device in this library
Example device init.

## Slide 10
Master Library
Every board-level hardware lib has a reinit procedure !!!
Example of a property, i.e. class variable

## Slide 11
Master Library
Two power modes, min and norm.
*will probably change
Handling and initiating different power modes is to be implemented in housekeeper.py task*** verify

## Slide 12
Sub library example

## Slide 13
Anatomy of a Task
This is a task that blinks the led.
It is a subclass of task from template_task.py
When the task is executed, it runs the code within main_task.
Pycubed.py is self.cubesat
See priority and frequency for setting when a task will run
The mainboard executes tasks via a task scheduler

## Slide 14: Current Progress (as of 6/1/21)
Mainboard is functional and all peripherals are coded in.
  A new design revision will be made soon with some new features and some pinout changes.
Payload interface board libraries in progress
  ~90% complete, waiting on some parts and another design rev for the final design
Tasks have been started, but nothing of substance there just trying to get a good background set up
Some PC/website software has been written.

## Slide 15: Things to Do:
Define operating states and what tasks should run at what times
Code high-level functionality
  i.e. all the tasks, commands, data handling
Define radio>mainboard>payload data exchange for target bitrate
Test it for extended periods extensively
Make sure all code written is executed successfully on ground
  Fault handling is EXTREMELY important in this application
Code pc host software to display live telemetry and simulate operations
Code PC ground station software

## Slide 16: Phase 1 Plan
Pair 1 will define and code simulation and data interface to host PC (main priority #2)
  We image a python program with a gui and real-time telemetry data updating, Marek started something like this but it really only uploaded new code to the device
Pair 2 will define and start to code the payload operation (main priority # 1)
  Will be discussed in a moment
Once host software is in a good state, it can start to be tested by Pair 1 Implementing the ADCS (main priority #3)

## Slide 17: USB Interface
Mainboard
Host PC
Usb_cdc.terminal
Usb_cdc.data
USB
Circuitpython REPL
All debug data is also printed here
Db_cdh and simulation handling
Circuitpython REPL terminal
Read debug data to display on GUI
Read/send cb_cdh and simulation commands

## Slide 18: Top Level Simulation / Debug Interface Flowchart
Usb connected?
Set all simulation flags to 0
Look at usb_cdc.data port for new command
No
Yes
Execute command if detected
Mainboard
Host PC
Debug Data Stream Output
Query host for simulation data
Value simulation flag True?
Send db_cdh commands to device from user GUI
Send queried simulation value over
Gather data from Debug data stream and display on GUI nicely

## Slide 19: REPL terminal and data stream
Regular circuitpython terminal.
Cubesat.debug prints data here
Print() command also prints here
Ctrl-C to end and ctrl-D to reload

## Slide 20: Debug command terminal
First asci encoded word “exec_cmd” is the keyphrase for the command to run
Then “ “ space for arguments passed
All arguments are separated by “arg0,arg1” comma right now, not “arg0, arg1“ comma space
Not implemented yet, but this is where the device will also ask for simulation data

## Slide 21: Main Operation Modes of Satellite
STARTUP MODE
SAFE MODE
IDLE MODE
PAYLOAD MODE
Each mode will have several substates.
Each mode/state will probably have specific tasks/ change task settings on the fly.
Runs once, x amount of time after initial deployment
Deploys deployables
Initial system checkout and startup
  i.e. ADCS detumble,
  ADCS calibrate,
  ETC.
Turns everything off, sleeps for x amount of time when it will re-check everything and try to re-enter idle mode.
Probably will beacon once for help during this. An override function may be implemented
Device in this mode most of time.
Will beacon over LoRa looking for commands from ground.
Payload will be powered off.
ADCS in point mode
Initiated from idle mode to start payload experiment.
Recieves data stream over LoRa for next arm/exec command
Sends data stream down of payload camera, arm, and important telemetry.
ADCS in payload_comp() mode, where it will hold and try to ignore arm torque exerted.
  If time, implement where cubesat will point at ground for better data transmission and reception.
A “frame”-like interface will probably have to be defined with a strict state machine, error handling, and no getting held up on lost data.

## Slide 22: STARTUP Mode
To-be Defined.

## Slide 23: Safe Mode

## Slide 24: Idle Mode

## Slide 25: Basic Radio Packet Structure
Header
1-4 bytes
CMD
1 byte
ARGs
1-x bytes
CRC
(ideally CRC-32)
4 bytes
Termination
1 byte

## Slide 26: Header Structure
Byte 1= packet no.
Byte 2 = number of packets in Tx
Byte 3b0 = crc flag
Byte 4 = nothing (can add more flags)

## Slide 27: Over the Air (OTA)(Radio) Commands
2 byte command code
Binary encoded, along with args passed.

## Slide 28: Minimum Functional Payload
Send Payload Init command w/ payload op settings
Send control data at x freq
Receive photo every after x transmissions
Send ACK
Send ACK response
add a flag to request to send a photo down after X rx’s
ACK
Send photo

## Slide 29: Payload Mode

## Slide 30: adcs_task.py

## Slide 31: payload_task.py

## Slide 32: db_cdh.py / usb_data_task.py
Debug commands sent via host PC
Also implement ability to run regular flight cdh.py commands with normal output over radio and debug info via USB.

## Slide 33: cdh.py
All of the “in flight” commands will go here.
i.e. setting persistent settings, imitating payload, printing log, printing telemetry, etc.
Some commands like exec, query, and hreset will probably have to be password-protected in addition?

## Slide 34: Beacon tasks
Idle mode beacon tasks for LoRa and Irridium.
Lora beacons at X frequency and Irridium beacons at X frequency. Both do CDH handling and can initiate a payload operation. TBR if iridium can handle a payload operation.

## Slide 35: Telemetry gathering tasks
Imu_task.py
  Reads IMU data and overwrites data in cubesat.data_buffer{“imu”}.
GPS_task.py
  Reads GPS data and overwrites data in cubesat.data_buffer{“gps"}
Temperature_task.py
  Reads various temperatures and overwrites data in cubesat.data_buffer{“temp”}
  Turns overheating devices off.
Time_task.py
  Prints time data.
Battery_task.py
  Gathers battery information and power readings. Initates safe mode if low battery is detected.

## Slide 36: Housekeeper task
Maybe break into a bunch of smaller tasks?
If a device has faulted out (happens more than you think!) it will attempt to reset the device(s) ~1x per hour?
Preforms a daily hard reset to the satellite
Other housekeeping tasks?
  gc_collect is already it’s own thing running at 2Hz